## Slide 1: Essential Home Maintenace for long term savings

## Slide 2: Purpose of Presentation
To help new and existing home owners understand the importance of maintaining all sytems within the home and how that can save the home owner in the long run,
Provide information on what needs to be maintained and tips to do so,

## Slide 3: Importance of regular home maintence
Regular home maintenance is critical for protecting what is often a person's largest financial asset and ensuring a safe living environment. Proactive upkeep can prevent small, manageable issues from escalating into catastrophic failures.

## Slide 4: Benefits of Home Maintenance
Financial Savings: Regular maintenance is significantly cheaper than major repairs. For instance, fixing a minor leak or cleaning gutters can prevent extensive water damage that costs thousands to remediate. Homeowners are often advised to budget 1% to 4% of their home's value annually for these recurring expenses.
1
Preservation of Property Value: A well-maintained home retains and increases its market value over time. Homes with high "curb appeal" (well-kept lawn, fresh paint, intact driveway) can attract higher offers and sell faster than neglected properties.
2
Enhanced Safety and Health: Routine checks ensure critical safety systems, such as smoke and carbon monoxide detectors, are functional. Maintenance also prevents health hazards like mold growth, pest infestations, and poor indoor air quality.
3
Increased Energy Efficiency: Servicing HVAC systems and sealing gaps around windows and doors reduces energy consumption, leading to lower monthly utility bills.
4
Extended Lifespan of Systems: Just as regular oil changes extend a car's life, routine servicing prolongs the lifespan of appliances and major systems like the roof, plumbing, and electrical wiring.
5

## Slide 5: Essential Categories of Home Maintenance
Safety Checks: Testing of alarms and security systems.
Seasonal Tasks: Tailoring work to the weather, such as Floridas Hurricane Season
Structural Upkeep: Monitoring the foundation, walls, and roof for cracks or leaks.
Appliance Care: Prevention of efficiency loss and fire hazards

## Slide 6: Time Frames for Home Maintenance
Monthly
Annually
Every 3-5 Years+
Spring
Summer
Fall
Winter

## Slide 7: Monthly Maintenance
Yard and Exterior
  Trees surrounding home for damage
Home exterior
  Gutters and downspouts
Home Interior
  Smoke /carbon monoxidealarms, fire extinguisher
Electrical
  Ground Fault Circuit interrupters (CDGI)
Heating and Cooling
  Chage AC Filters, check vents for bloackage
Plumbing
  Drain traps for hair (sink and shower)
  Clear mineral deposits in facets and showerheads
  Softner systemre
Appliance Maintenance
  Clean Dryer vents
  Clean refrigerator coils
  Check and clean kitchen drains and garbage disposal
  Clean kitchen vent, hood and filter
  Clean oven& range, dishwasher filter and washing machine.

## Slide 8: Annual Maintenance
Home Exterior
Roof Inspection
Inspect and clean brick masonry
Clean windowns and screens
Lubricate window and door hinges
Home Interior
Carpets or hardwood
Heating and Cooling
Have AC system inspected and serviced
Plumbing
Inspect toilet supply lines, valves, and parts

## Slide 9: 3-5 Year Maintenance
Plumbing
Have septic tank inspected ( if applicable)
If needed have septic tank pumped by septic system expert
Applicances
Replace Washing machine hoses

## Slide 10: Spring Maintenance
Yard and Exterior
Inspect all fences to make sure it is intact (pool and yard)
Check for signs of pests
Trim trees, bushes and shrubs away from house.
Test sprinkler system
Home Exterior
Clean gutters and downding joi spouts-make sure dowb spouts frain 4ft from the home
Check condition of rood shingles
Check weather stripping on all doors and windows. Replace as needed
Check and re-caulk windows and doorsm sliding joints, and anywhere else needed.
Home Interior
Change batteries in alarm and dectection systems
Check operation of windows and doors
Plumbing
Check drain and supply lines for leaks
Appliances
Clean exhaust dan outlets and screens
Garage
Lubricate door rollers and door tracks
Attic
Inspect the ductwork and ventilation

## Slide 11: Summer Maintenance
Yard and Exterior
Insoect driveway, landings, porchs, and patios for cracks and repair as needed.
Inspect and repair decks as needed
Home Exterior
Look for peeling paint or caulk and repair as needed
Re-nail loose siding and trim when needed
Check for rotting wood and get replaced as needed
Check for foundation issues
Home Interior
Test home security system
Reverse ceiling fans counterclockwise
Electrical
Check for damaged electrical cord
Appliances
Deep clean dishwasher
Garage
Ensure thr garage door works properly such as emergency stop
Check for water damage
Check for signs of pests

## Slide 12: Fall Maintenance
Yard and Exterior
Inspect fences to ensute they are still intact
Check for pests
Trim trees, bushes, and shrubs
Lawn maintenance
Home Exterior
Clean gutters and down spouts
Check roof shingles (hard to do during hurricane season)
Attic vents
Check weather stripping on all windows and doors replace qs needed
Heating and Cooling
Ensure ist is working properly (test heat)
Plumbing
Flush water heater and check for leals
Check drains and supply lines for leaks
Garage
Ensure proper stoage of fuel cans
:ubricate gatage door rollers and traks
Attic
Check for signs of pests
Check for water damage (especially after hurricane season)
Wnsure insulation is in place

## Slide 13: Winter Maintenance
Home Interior
Reverse ceiling fans clockwise
Repair and repaint interior wall damage asb needed
Inspect shower/tub for signs of damage
Check and re-caulk tile in all bathroom and kitchen areas as needed.
Electrical
Check for damaged electrical cords
Test Ground Fault Circuit Interrupters (GFCI)
Appliances
Inspect washing maching hoses and connections
Inspect dishwasher hoses for leaks
Inspect and clean refrigerator drip pan and icemaker connections

## Slide 14: DIY Home Maintenance Tips
Essential Monthly Tasks
HVAC Filters: Clean or replace air filters every 30 to 90 days to ensure system efficiency and better air quality.
Safety Detectors: Test smoke and carbon monoxide detectors monthly by pressing the "test" button.
Garbage Disposal: Clean by grinding ice cubes and citrus peels, then flushing with baking soda and vinegar to eliminate odors.
Unused Fixtures: Run water and flush toilets in guest bathrooms or basements to keep traps full and prevent sewer gases from entering the home.
Annual Proactive Maintenance
Water Heater Flush: Drain a few gallons from the tank to remove sediment buildup, which helps maintain heating efficiency and extends the unit's lifespan.
Garage Doors: Lubricate moving parts (tracks, rollers, and hinges) to ensure smooth operation and reduce noise.
Dryer Vents: Use a specialized brush to deep-clean the entire dryer vent duct to prevent potential house fires.

## Slide 15: DIY Home Maintenance Continued
Seasonal Upkeep
Gutters: Clean debris twice a year (Spring and Fall) to prevent water damage to the foundation and roof.
Exterior Plumbing: Before winter, disconnect hoses, drain exterior faucets, and install insulated covers to prevent frozen or burst pipes.
Appliance Maintenance: Vacuum refrigerator condenser coils annually to improve cooling efficiency and extend appliance life.
Window Seals: Inspect and replace worn weatherstripping or caulk around windows and doors to reduce drafts and lower energy bills.
Simple Beginner Repairs
Leaky Faucets: Most leaks are caused by a worn-out rubber washer that can be easily replaced after turning off the water supply.
Running Toilets: Test for leaks by adding food coloring to the tank; if color appears in the bowl, you may only need to replace the flapper.
Drywall Patching: Use a small container of spackle and a putty knife to fill minor nail holes or small cracks.
Cabinet Refresh: Replacing outdated knobs or pulls is one of the simplest ways to modernize a kitchen or bathroom.

## Slide 16: Home Warranties in relation to Home Maintenance
Best time to purchase a home warranty is when you purchase your home or when existing manufacturer warranties are set to expire.
Home warranties are designed to cover mechanical failures due to normal wear and tear, meaning they exclude many types of damage, specific structural components, and certain high-end systems.

## Slide 17: Common Things not covered with Home Warranties
1. Condition and Maintenance Issues
Pre-existing Conditions: Problems that existed before coverage began—especially those noted in a home inspection or visible upon a basic mechanical test—are typically excluded. Some plans may cover "unknown" pre-existing conditions if they were not detectable during a visual inspection.
Lack of Maintenance: Failures caused by neglecting routine upkeep (e.g., not changing HVAC filters or flushing water heaters) can lead to denied claims.
Improper Installation or Code Violations: Systems that were installed incorrectly or do not meet local building codes at the time of failure are often not covered.
2. Damage Types
Cosmetic Issues: Scratches, dents, chipped paint, or other aesthetic defects that do not affect the functionality of an appliance are not covered.
Secondary or Consequential Damage: A home warranty covers the repair of the broken item itself, but not the damage it causes. For example, it might fix a leaking dishwasher but will not cover the water damage to your kitchen floors.
Acts of Nature: Damage from floods, earthquakes, fire, or storms is excluded and is typically handled by homeowners insurance.
Pest Damage: Damage caused by termites, rodents, or other pests is generally not covered.

## Slide 18: Common Things not covered with Home Warranties Continued
3. Specific Items and Components
Structural Components: The home's "envelope"—including the foundation, walls, windows, doors, and flooring—is excluded.
Outdoor and Non-Essential Items: Items like sprinkler systems, outdoor kitchens, pools, spas, and septic tanks are usually excluded unless you purchase specific optional add-on coverage.
Small Appliances: Handheld or countertop appliances like toasters, coffee makers, and blenders are not covered.
Commercial-Grade Equipment: High-end, professional, or commercial-grade appliances (e.g., Sub-Zero or Thermador) are often excluded from standard plans.
Items Under Manufacturer Warranty: Providers will often not cover an item if it is still protected by its original manufacturer's warranty
4. Coverage Limits and Access
Payout Caps: Most plans have a "per-item" or "per-term" dollar limit. If a repair exceeds this cap (e.g., a $1,500 limit for an HVAC repair that costs $2,500), you must pay the difference.
Inaccessible Units: Claims may be denied if the technician cannot safely reach the appliance or system without moving walls or major structural changes

## Slide 19: Home Warranty Companies
Liberty Home Guard
(833) 544-8273
www.libertyhomegaurd,com
First American Home Warranty
(844) 586-1025
go.fahw.com
American Home Shield
(844)253-1922
www.ahs.com
Select Home Warranty
(855) 718-1368
shw.selecthomewarranty.com
Choice Home Warranty
(888) 373-8047
www,choucehomewarranty.com

## Slide 20: Questions